## Slide 1
Joel Fenolio, P.E.
Upper Columbia Senior Water Manager
11 May 2016
Kootenai Basin Spring/SummerOperations for 2016

## Slide 2
Atmospheric river
intense, focused, steady rainfall
with high snow levels
Atmospheric river
intense, focused, steady rainfall
with high snow levels

## Slide 3
Atmospheric river
intense, focused, steady rainfall
with high snow levels
Atmospheric river
intense, focused, steady rainfall
with high snow levels
April record warmth and dry
Snowpack drops
well below normal in a month
Bonners Ferry: Warmest April on record
With warmth, rapid snowmelt in April
Now less snowmelt and with dry weather: Runoff decreases

## Slide 4: Snowpack Story for 2016

## Slide 5: Libby Dam Apr-Aug May Inflow Forecast
Corps forecast is 5.8 MAF (99% or average)
  5900 KAF is the average Apr-Aug inflow volume

## Slide 6: BiOp Requirements and Habitat Operations
Libby WSF of 5.8 MAF sets the following:
  Sturgeon Volume of 0.93 MAF
    As measured above 4 kcfs
  Bull Trout Minimum after the pulse through August 31st is 7 kcfs
Habitat Operations
  6 kcfs minimums in Sept
  Target 2449 ft end of August rather than end of Sept

## Slide 7: Moderate ESP Inflow Scenario
Refill end of July
2449 ft end of August
7.8 kcfs flat flow
0.93 MAF Sturgein Pulse
Notes: Will be updated next week

## Slide 8: Dry Inflow Scenario
0.93 MAF Sturgein Pulse
Refill end of July
Below 2449 ft end of August
7 kcfs flat flow

## Slide 9: Summary
Timing of Inflows shifted up by 4 to 6 weeks
Flood Risk low – based on the below average snowpack
Libby Dam will likely not refill to 2452 to 2454 feet this summer
  Anticipated timing of refill late July to August
  Seattle District is currently looking at refilling earlier than late July
June precipitation is the wild card in terms of flood risk and refill