## Slide 1: Smolt Survival and Travel Time & Transportation Analyses Update with 2016 Data
Northwest Fisheries Science Center
Steven G. Smith
December 7, 2016
Technical Management Team
2016 Year-End Review

## Slide 2
Summary of migration conditions, travel time and survival of PIT-tagged smolts through the hydropower system in 2016
  September 26 Memo; Draft report to BPA in prep
    Only those fish left to migrate in-river
    Only juvenile data, not survival to adult
Outline

## Slide 3
  Above average flow early, tailed off
  Average spill percentage
  Water warmer than average (1-1.5o C throughout)
  Short travel times (high migration rate) in April
  Small percentage (<25%) transported
2016 Spring Conditions

## Slide 4
Chinook survival from hatchery to LGR above 70% third year in a row
Reach-by-reach mix of higher and lower than average
Overall hydrosystem survival about 3-4% lower than average for both species
Deficit in lower Columbia for both species
2016 Spring Survival

## Slide 5
Bonneville
The Dalles
John Day
Hells Canyon
Oxbow
Brownlee
Priest Rapids
Wanapum
Rock Island
Rocky Reach
Wells
Chief Joseph
Grand Coulee
McNary
Ice Harbor
Little Goose
Lower Granite
Lower Monumental
Juvenile detectors
Snake R. trap
PIT-tag Data Sources
PIT tag
trawl
Hatchery
Releases
Hatchery &
Trap Releases
Notes: Map etc.

## Slide 14
BON
TDA
95.6
91.2
79.6
87.1
93.6
87.2
93.6
92.9
94.2
88.3
82.4
87.1
MCN
JDA
LMO
LWG
LGS
SRT
BON
JDA
MCN
LMO
LGS
LWG
SRT
Yearling
Chinook salmon
reach survival
2016
Mean 02-16
93.3 (90.6)
93.4 (93.3)
IHR
Notes: Source: for most recent year: Table 25 of Report (Table 16 for LMO-ICE, ICE-MCN)
For average: sgs’s “Clean S” spreadsheet – averages for 2002-2011

## Slide 15
BON
TDA
IHR
99.0
91.8
92.7
70.9
99.8
81.3
96.9
93.1
91.4
85.1
81.2
77.9
MCN
JDA
LMO
LWG
LGS
SRT
BON
JDA
MCN
LMO
LGS
LWG
SRT
Steelhead
reach survival
2016
Mean 02-16
84.2 (89.7)
90.2 (88.1)
Notes: Source: for most recent year: Table 25 of Report (Table 16 for LMO-ICE, ICE-MCN)
For average: sgs’s “Clean S” spreadsheet – averages for 2002-2011

## Slide 23: Smolt Transportation Seasonal Analyses
Yearling Chinook & Steelhead
Migration Years 2011-2014
      Updated with adult returns through Nov 17, 2016
      Added smolt migration year 2014
      New accounting (“adult currency”)

## Slide 24: Estimating Patterns of SAR vs. Date
Need a “time-stamp” – date of passage/detection
These analyses use fish that entered JBS at Lower Granite Dam
  tagged upstream or at the dam
  either transported (T) or bypassed (B or “C1”)
  can adjust “standards” based on observed C0 > C1

## Slide 31: “Adult Currency”
What do all these percentages and ratios of percentages mean
in terms of numbers of returning adults?

## Slide 32: Data Sources for “Adult Currency”
Smolt Monitoring Program – “Collection Count”
  Estimate of the number of fish (tagged + untagged) in the JBS
  (Wild and hatchery steelhead not counted separately)
Daily detection probability estimates from PIT tags
  - Estimate of the proportion of all passing fish that entered JBS
Model-Averaged estimates of SARs for transported and bypassed

## Slide 33
Total arrived at LGR = 1.12 million
Total entered JBS during transport ops = 234,000

## Slide 34
Total arrived at LGR = 1.12 million
Total entered JBS during transport ops = 234,000

## Slide 35
Total arrived at LGR = 1.12 million
Total entered JBS during transport ops = 234,000
Total adults from bypassed smolts in April = 1,170
Total adults from transported smolts in May = 3,985
“Hypothetical” adults if smolts in JBS in May
had been bypassed = 3,105

## Slide 36: “Adult Currency” – Transported vs. Bypassed
Assumptions
  Bypass percentages and SARs estimated from PIT-tagged fish apply to untagged fish
  Spill levels and Transportation start date stay the same (not trying to model these!)
  SARs during transport period would not change with different mixture of transported and bypassed fish
  15% of total steelhead passage is wild
  Everything estimated with no error
  (i.e., haven’t yet done the work to characterize error in estimation)
  “Conservative” modeling effort

## Slide 37
Wild Chinook - Smolts

## Slide 38: “Adult Currency” – Transported vs. Bypassed Wild Chinook – Lower Granite Dam Mean difference for LGR = 1,033

## Slide 39: “Adult Currency” – Transported vs. Bypassed Wild Chinook – Lower Granite Dam Mean difference for LGR = 1,033 Still to come: estimates for Little Goose, Lower Monumental

## Slide 40: “Adult Currency” – Transported vs. Bypassed Wild Chinook – Lower Granite Dam Mean difference for LGR = 1,033 Still to come: estimates for Little Goose, Lower Monumental
Mean difference for Hatchery Chinook from Lower Granite Dam = 5,951

## Slide 41
Wild Steelhead - Smolts

## Slide 42: “Adult Currency” – Transported vs. Bypassed Wild Steelhead – Lower Granite Dam Mean difference for LGR = 2,288

## Slide 43: “Adult Currency” – Transported vs. Bypassed Wild Steelhead – Lower Granite Dam Mean difference for LGR = 2,288
Mean difference for Hatchery Steelhead from Lower Granite Dam = 7,080

## Slide 44: Smolt Transportation Seasonal Analyses
Subyearling Fall Chinook Salmon
Study in Migration Years 2006, 2008-2012
      Adults complete except for handful of 5-oceans expected in 2017
      Draft report IMMINENT

## Slide 45: Types of fall Chinook salmon
Natural
  - Not enough of these to conduct a transportation evaluation
Hatchery production subyearlings
Hatchery production yearlings
  Released in early April, pass dams before spring transportation program begins.
Hatchery-reared surrogates for natural fish
  Lyons Ferry fish specially reared at Irrigon and Dworshak NFH etc.

## Slide 50: Summary of T:B analyses by dam
Seasonal tendencies for surrogate subyearlings:
  Migrate throughout summer and into fall and winter (esp. Clearwater releases)
  SAR for bypassed fish increases from earliest to latest
  SAR for Transported fish also increases, but has a peak around September 1
  Early-arriving minority have higher SAR if Bypassed, all others if Transported
  Switch occurs early-to-mid July

## Slide 54: Summary of T:B analyses by dam
Seasonal tendencies for production subyearlings:
  Migrate mostly in June, a minority into July
  Late-arriving minority have higher SAR if Transported, all others if Bypassed
  Switch occurs mid-to-late June

## Slide 55: Smolt Transportation Analyses
Sockeye Salmon
Migration Years 2009-2014
Return Years 2011-2016
      Annual Returns to Bonneville, McNary, and Lower Granite

## Slide 56
Sockeye Transportation
Smolts at LGR to Adults to Bonneville Dam |  |  | 
Migration Year | Transported @ LGR | Bypassed @ LGR | T:B (95% bootstrap CI)
2009 | 134 / 4272 = 3.14% | 45 / 3041 = 1.49% | 2.11 (1.54 – 3.05)
2011 | 26 / 3151 = 0.83% | 24 / 8548 = 0.28% | 2.94 (1.67 – 5.24)
2012 | 80 / 6523 = 1.23% | 17 / 4334 = 0.40% | 3.10 (1.96 – 5.78)
2013 | 303 / 6047 = 5.01% | 117 / 5563 = 2.11% | 2.38 (1.94 – 2.96)
2014 | 35 / 2891 = 1.22% | 10 / 1671 = 0.61% | 2.00 (1.07 – 4.73)
Mean/ Geomean | 2.29 | 0.98 | 2.47 (2.02 – 3.21)

## Slide 57
Sockeye Transportation
Smolts at LGR to Adults to Lower Granite Dam |  |  | 
Migration Year | Transported @ LGR | Bypassed @ LGR | T:B (95% bootstrap CI)
2009 | 84 / 4272 = 1.97% | 28 / 3041 = 0.93% | 2.13 (1.42 – 3.40)
2011 | 4 / 3151 = 0.13% | 11 / 8548 = 0.13% | 1.01 (0.20 – 2.71)
2012 | 29 / 6523 = 0.45% | 8 / 4334 = 0.19% | 2.37 (1.20 – 6.46)
2013 | 16 / 6047 = 0.27% | 13 / 5563 = 0.24% | 1.13 (0.53 – 2.56)
2014 | 13 / 2891 = 0.46% | 8 / 1671 = 0.49% | 0.93 (0.39 – 2.66)
Mean/ Geomean | 0.65 | 0.39 | 1.40 (0.91, 2.08)

## Slide 58
Sockeye Transportation
Adult Conversion Rate – Bonneville To McNary |  |  | 
Return Year | Transported @ LGR | Bypassed @ LGR | Ratio (95% bootstrap CI)
2011 | 80 / 127 = 63.0% | 28 / 45 = 62.1% | 1.01 (0.79 – 1.35)
2013 | 16 / 34 = 47.1% | 18 / 22 = 81.3% | 0.58 (0.36 – 0.85)
2014 | 43 / 89 = 48.3% | 19 / 25 = 75.6% | 0.64 (0.47 – 0.88)
2015 | 13 / 283 = 4.6% | 30 / 110 = 27.3% | 0.17 (0.08 – 0.30)
2016 | 17 / 37 = 46.0% | 10 / 11 = 89.5% | 0.51 (0.33 – 0.75)
Mean/ Geomean | 41.8% | 57.2% | 0.50 (0.41 – 0.60)

## Slide 59
Sockeye Transportation
Adult Conversion Rate – McNary to Lower Granite |  |  | 
Return Year | Transported @ LGR | Bypassed @ LGR | Ratio (95% bootstrap CI)
2011 | 75 / 80 = 93.6% | 28 / 28 = 98.8% | 0.95 (0.88 – 1.00)
2013 | 6 / 16 = 37.8% | 10 / 18 = 55.5% | 0.68 (0.27 – 1.40)
2014 | 41/ 43 = 95.0% | 14 / 19 = 73.3% | 1.30 (1.03 – 1.81)
2015 | 0 / 13 = 2.6% | 8 / 30 = 26.9% | 0.10 (0.06 – 0.19)
2016 | 13 / 17 = 81.7% | 8 / 10 = 79.0% | 1.03 (0.73 – 1.63)
Mean/ Geomean | 62.1% | 66.7% | 0.61 (0.48 – 0.78)

## Slide 60: Questions?