## Slide 1: Smolt Survival and Travel Time & Transportation Analyses Update with 2017 Data
Northwest Fisheries Science Center
Steven G. Smith
December 12, 2017
Technical Management Team
2017 Year-End Review

## Slide 2
Migration conditions, travel time and survival of PIT-tagged smolts through the hydropower system in 2017
  September 18 Memo; Draft report to BPA in prep
    Only those fish left to migrate in-river
    Only juvenile data, not survival to adult
Outline

## Slide 3
  High flow, especially in early season
  High spill percentage
  Water warmer than average (0-1o C throughout)
  Shorter than average travel times
    Shorter than low-flow 2015 and similar to average-flow 2016
  Small percentage (<25%) transported
2017 Spring Conditions

## Slide 4
Chinook survival from hatchery to LGR near average 65%
Reach-by-reach mix of higher and lower than average
Overall hydrosystem survival below average (~6%) for 3rd or 4th consecutive year
Deficit in lower Columbia for both species
  (some data concerns)
2017 Spring Survival

## Slide 5
Bonneville
The Dalles
John Day
Hells Canyon
Oxbow
Brownlee
Priest Rapids
Wanapum
Rock Island
Rocky Reach
Wells
Chief Joseph
Grand Coulee
McNary
Ice Harbor
Little Goose
Lower Granite
Lower Monumental
Juvenile detectors
Snake R. trap
PIT-tag Data Sources
PIT tag
trawl
Hatchery
Releases
Hatchery &
Trap Releases
Notes: Map etc.

## Slide 16
BON
TDA
91.6
90.8
72.0
87.2
NA
91.2
93.6
93.3
94.0
87.2
82.7
87.2
MCN
JDA
LMO
LWG
LGS
SRT
BON
JDA
MCN
LMO
LGS
LWG
SRT
Yearling
Chinook salmon
reach survival
2017
Mean 02-17
93.4 (90.8)
95.5 (93.4)
IHR
Notes: Source: for most recent year: Table 25 of Report (Table 16 for LMO-ICE, ICE-MCN)
For average: sgs’s “Clean S” spreadsheet – averages for 2002-2011

## Slide 17
BON
TDA
IHR
96.2
94.3
94.1
64.3
NA
84.9
97.0
94.4
91.6
85.7
80.0
78.3
MCN
JDA
LMO
LWG
LGS
SRT
BON
JDA
MCN
LMO
LGS
LWG
SRT
Steelhead
reach survival
2017
Mean 02-17
80.2 (89.1)
92.1 (88.3)
Notes: Source: for most recent year: Table 25 of Report (Table 16 for LMO-ICE, ICE-MCN)
For average: sgs’s “Clean S” spreadsheet – averages for 2002-2011

## Slide 25
Questions

## Slide 26: Smolt Transportation Seasonal Analyses
Yearling Chinook & Steelhead
Migration Years 2013-2015
      Updated with adult returns through Nov 21, 2017
      Added smolt migration year 2015
      SAR and T:B data LGR, LGS, and LMN
      “Adult currency” for all three dams, MY 2006-2015

## Slide 27: Estimating Patterns of SAR vs. Date
Need a “time-stamp” – date of passage/detection
These analyses use fish that entered JBS at Lower Granite Dam
  tagged upstream or at the dam
  either transported (T) or bypassed (B or “C1”)
  can adjust “standards” based on observed C0 > C1

## Slide 28: Summary / Conclusions
2013: Not much benefit for wild Chinook at any dam;
    Benefit for Steelhead at all 3 dams
2014: T:B ratio > 4 for wild Chinook at LGR, lower elsewhere
    T:B ratio between 2 and 3 for Steelhead at all 3 dams
2015: SAR ~ 1.0% for transp. wild Chinook;
    near 0% for wild Chinook bypassed in May
Poor data for wild Steelhead

## Slide 29: Summary / Conclusions
Results tend to be similar for Lower Granite and Little Goose Dams
  About 75-80% of transported fish
Lower Monumental: fewer fish transported, less PIT-tag data,
  lower T:B ratios (often ~ 1.0)

## Slide 30: Summary / Conclusions
Less seasonality in T:B ratios in recent years (lines flatter)
More fish migrating in April in recent years
  - More than 10 years since we last gathered substantial transport data from April-migrating fish

## Slide 31: A Note on Zero Adult Counts “If nothing goes right, is everything all wrong?”
Median Unbiased Estimator of Binomial Probability
  10 trials, no successes: MUE = 3.35%
  100 trials, no successes: MUE = 0.345%
  1000 trials, no successes: MUE = 0.0345%
10,000 trials, no successes: MUE = 0.00347%

## Slide 32: 2013

## Slide 39: 2014

## Slide 46: 2015

## Slide 50: Lower Granite Dam Totals for May 1 – June 4, 2015
Wild Chinook |  |  |  |  |  | Wild Steelhead |  |  | 
 | Juv | Adt | SAR | CI |  | Juve | Adt | SAR | CI
Transport | 680 | 8 | 1.20 | 0.47-2.08 |  | 748 | 1 | 0.16 | 0.05-0.56
Bypassed | 873 | 0 | 0.04 | 0.00-0.34 |  | 580 | 1 | 0.20 | 0.06-0.72
T:B Ratio |  |  | 30.3 | 4.5 – 48.8 |  | T:B Ratio |  | 0.78 | 0.08-7.10

## Slide 51: Little Goose Dam Totals for May 1 – June 4, 2015
Wild Chinook |  |  |  |  |  | Wild Steelhead |  |  | 
 | Juv | Adt | SAR | CI |  | Juve | Adt | SAR | CI
Transport | 829 | 9 | 1.11 | 0.50-1.83 |  | 755 | 1 | 0.16 | 0.05-0.55
Bypassed | 2110 | 1 | 0.06 | 0.02-0.20 |  | 801 | 1 | 0.15 | 0.04-0.52
T:B Ratio |  |  | 19.7 | 4.9-104.0 |  | T:B Ratio |  | 1.06 | 0.12-9.71

## Slide 52: Lower Monumental Dam Totals for May 1 – June 4, 2015
Wild Chinook |  |  |  |  |  | Wild Steelhead |  |  | 
 | Juv | Adt | SAR | CI |  | Juve | Adt | SAR | CI
Transport | 333 | 0 | 0.10 | 0-0.90 |  | 224 | 0 | 0.15 | 0-1.34
Bypassed | 758 | 0 | 0.05 | 0-0.40 |  | 190 | 0 | 0.18 | 0-1.58
T:B Ratio |  |  | NA | NA |  | T:B Ratio |  | NA | NA

## Slide 53: “Adult Currency”
What do all these percentages and ratios of percentages mean
in terms of numbers of returning adults?

## Slide 54: Data Sources for “Adult Currency”
Smolt Monitoring Program – “Collection Count”
  Estimate of the number of fish (tagged + untagged) in the JBS
  (Wild and hatchery steelhead not counted separately)
Daily detection probability estimates from PIT tags
  - Estimate of the proportion of all passing fish that entered JBS
Model-Averaged estimates of SARs for transported and bypassed

## Slide 55
Total arrived at LGR = 1.12 million
Total entered JBS during transport ops = 234,000

## Slide 56
Total arrived at LGR = 1.12 million
Total entered JBS during transport ops = 234,000

## Slide 57
Total arrived at LGR = 1.12 million
Total entered JBS during transport ops = 234,000
Total adults from bypassed smolts in April = 1,170
Total adults from transported smolts in May = 3,985
“Hypothetical” adults if smolts in JBS in May
had been bypassed = 3,105

## Slide 58: “Adult Currency” – Transported vs. Bypassed
Assumptions
  Bypass percentages and SARs estimated from PIT-tagged fish apply to untagged fish
  Spill levels and Transportation start date stay the same (not trying to model these!)
  SARs during transport period would not change with different mixture of transported and bypassed fish
  15% of total steelhead passage is wild
  Everything estimated with no error
  (i.e., haven’t yet done the work to characterize error in estimation)

## Slide 59: “Adult Currency” – Transported vs. Bypassed Wild Chinook – Lower Granite Dam Mean difference for LGR = 1019

## Slide 60: “Adult Currency” – Transported vs. Bypassed Wild Steelhead – Lower Granite Dam Mean difference for LGR = 2,221

## Slide 61: “Adult Currency” – Transported vs. Bypassed Lower Granite Dam

## Slide 62: “Adult Currency” – Transported vs. Bypassed Little Goose Dam

## Slide 63: “Adult Currency” – Transported vs. Bypassed Lower Monumental Dam

## Slide 64: “Adult Currency” – Transported vs. Bypassed 2006-2015 Mean difference between transported estimate and hypothetical bypassed
Species x Rear Type | Lower Granite | Little Goose | Lower Moumental
Wild Chinook | 1,019 | 742 | 95
Wild Steelhead | 2,221 | 3,794 | 1,427
Hatchery Chinook | 5,230 | 3,024 | 1,504
Hatchery Steelhead | 5,507 | 6,718 | 4,147

## Slide 65
Questions

## Slide 66: Smolt Transportation Seasonal Analyses
Subyearling Fall Chinook Salmon
Study in Migration Years 2006, 2008-2012
      Adults complete except for handful of 5-oceans expected in 2017

## Slide 67: Types of fall Chinook salmon
Natural
  - Not enough of these to conduct a transportation evaluation
Hatchery production subyearlings
Hatchery production yearlings
  Released in early April, pass dams before spring transportation program begins.
Hatchery-reared surrogates for natural fish
  Lyons Ferry fish specially reared at Irrigon and Dworshak NFH etc.

## Slide 72: Summary of T:B analyses by dam – Fall Chinook
Seasonal tendencies for surrogate subyearling fall Chinook:
  Migrate throughout summer and into fall and winter (esp. Clearwater releases)
  SAR for bypassed fish increases from earliest to latest
  SAR for Transported fish also increases, but has a peak around September 1
  Early-arriving minority have higher SAR if Bypassed, all others if Transported
  Switch occurs early-to-mid July

## Slide 76: Summary of T:B analyses by dam – Fall Chinook
Seasonal tendencies for production subyearling fall Chinook:
  Migrate mostly in June, a minority into July
  Late-arriving minority have higher SAR if Transported, all others if Bypassed
  Switch occurs mid-to-late June

## Slide 77
Questions