## Slide 1: Libby dam sturgeon operations 2024
Date: 08 May 2024

## Slide 2
Minimum Reservoir Elevation
2415.46 ft on Mar 19, 2024
May VarQ 14.2 kcfs
Forecast Values are
Conceptual Plan
Full QPHC for start
of sturgeon pulse
Sturgeon Pulse Volume

## Slide 3: MAY 1st Water Supply Forecast and biop objectives
April-August inflow forecast for Libby Dam is 5.13 million acre-feet (MAF)
    Forecast is 82% of average
    Sturgeon Volume is 0.8 MAF
    Bull trout minimum flows following the Sturgeon Pulse through Aug 31 is 7 kcfs
  Libby Water Supply Forecast Trend:
    Libby flow augmentation draft to 10 ft from full (2449 ft) end of September

## Slide 5
Flow Augmentation PLAN
Spring Refill Began on May 1st
Sturgeon augmentation flow modeled to start on May 18th and ramp up discharges from Libby Dam to ~25 kcfs (powerhouse capacity). Maintain powerhouse pulse discharge for approximately ~17* days, followed by a relatively quick recession to an approximate flat to descending summer flow.
  Target to Maintain Bonners Ferry at or above 30 kcfs: ~18 Days (Median)
  Likely unable to maintain Bonners Ferry stage at or above 1760’
Decrease discharge (post-powerhouse pulse) at Libby Dam to summer flat flow following BiOp ramping rates.
  Lake Koocanusa End of September Target is 2449.0 ft, depending upon inflows
  * in season management and observed inflows may cause these values to change.

## Slide 7
VarQ Flow 14.3 kcfs
Sturgeon Pulse Volume

## Slide 8
1760 ft Goal
0 Days Median

## Slide 9
30 kcfs Goal
18 Days Median

## Slide 11
SUMMARY OF PLANNED REFILL OPERATIONS
Spring Refill Began on May 1st
Sturgeon augmentation flow modeled to start on May 18th and ramp up discharges from Libby Dam to ~25 kcfs (powerhouse capacity). Maintain powerhouse pulse discharge for approximately ~17* days, followed by a relatively quick recession to an approximate flat to descending summer flow.
  Target to Maintain Bonners Ferry at or above 30 kcfs: ~18 Days (Median)
  Likely unable to maintain Bonners Ferry stage at or above 1760’
Decrease discharge (post-powerhouse pulse) at Libby Dam to summer flat flow following BiOp ramping rates.
  Lake Koocanusa End of September Target is 2449.0 ft, depending upon inflows
  * in season management and observed inflows may cause these values to change.

## Slide 12: Questions?