## Slide 1
Brian Bangs, Paul Scheerer, and Shaun Clements
Native Fish Investigations Project Oregon Department of Fish and Wildlife
Effects of the Fall Creek reservoir drawdowns on downstream off-channel habitats

## Slide 2: Quick Oregon Chub Updates
Proposed delisting: Feb. 2014
Final delisting: Feb. 17, 2015
Post-delisting monitoring
  Nine year period
  Track distribution, abundance, and monitor threats

## Slide 3: Quick Oregon Chub Updates
OPB Oregon Field Guide
Feb. 26 at 8:30 PM
Army Corp’s Greg Taylor interview

## Slide 4: Fall Creek Drawdown Study
ACOE experimenting with reservoir drawdown (run of river operation)
Facilitate downstream movement of juvenile salmonids
  Economical alternative
  Huge sediment load enters river downstream as new channel carved into reservoir bed

## Slide 5: Fall Creek Drawdown Study
Concerns about effects of Fall Creek Drawdown on off-channel habitats and fish communities

## Slide 6: Fall Creek Drawdown Study
Monitor changes related to Fall Creek Reservoir drawdown
  Habitat, fish assemblage
Selected 4 sites to study with Floodplain Study methods

## Slide 7: Approach
Monitor water levels
2) Monitor temperatures
3) Determine the relationships between water levels and habitat availability (pond volume)
4) Identify the points of hydrologic connection
Notes: Could we add PIT-tag study?

## Slide 8: Approach
5) Determine changes in substrate
  Remap bathymetry
6) Describe Fish Assemblages
  Describe composition of fish assemblages (species diversity and abundance), natives vs. non-natives

## Slide 9
Goal
Determine the effect of drawdowns on:
Bathymetry (sedimentation),
Habitat characteristics,
Temperature regimes,
Timing, frequency, duration, magnitude of connection, and
Fish assemblage structure in off-channel habitats in Fall Creek, below the reservoir

## Slide 11: Bathymetry Mapping

## Slide 12: Bathymetry mapping

## Slide 13: Bathymetry mapping

## Slide 14: Remapping
2012
2013
2014
Annual mapping at each site

## Slide 15: What is it good for?
P
With piezometer:
Points of connection
Area
Volume
Average depth (Volume/Area)
Max. depth

## Slide 16: Depth Frequency Analysis
Convert TIN map to raster grid
Each cell 0.1 m2, and contains elevation data
-2.5
-2.1
-1.6
-1.1
-2.1
-1.8
-2.3
-1.9
-0.9
-1.3
-0.5
-1.0
Grid is not to scale!

## Slide 17: Depth frequency analysis
High terrace – shallow end
Max depth – deep end

## Slide 18: Depth frequency analysis
High terrace – shallow end
Max depth – deep end

## Slide 19: Depth frequency analysis

## Slide 20: Depth frequency analysis

## Slide 21: Depth frequency analysis
Detect change in area and volume

## Slide 22: Depth frequency analysis
High initial sedimentation, slow scouring

## Slide 23: Depth frequency analysis
Sedimentation
Gradual scour

## Slide 24: Depth frequency analysis
Mixed bag
Initial sedimentation low
Some scour

## Slide 25: Habitat at average summer depth
 | Area (m2) |  |  |  |  | Volume (m3) |  | 
Location | 2012 | 2013 | 2014 |  |  | 2012 | 2013 | 2014
Baumann | 1,344 | 104 | 400 |  |  | 757 | 32 | 119
Simpson | 209 | 868 | 1,031 |  |  | 25 | 201 | 290
Brewer | 1,177 | 611 | 203 |  |  | 153 | 82 | 35
Fall Cr. Conf. | 374 | 326 | 258 |  |  | 86 | 37 | 52
In 2013:
62% reduction in wetted area
66% reduction in water volume
3 locations area and vol. reduced, 1 greater
Notes: ADD RANGE

## Slide 26: Differences: 2012 and 2013 Drawdown
2012
High flow
Lots of silt/sand
No big flow events
2013
Lower flow, frozen
Less silt/sand
High flows following

## Slide 29: Habitat at average summer depth
 | Area (m2) |  |  |  |  | Volume (m3) |  | 
Location | 2012 | 2013 | 2014 |  |  | 2012 | 2013 | 2014
Baumann | 1,344 | 104 | 400 |  |  | 757 | 32 | 119
Simpson | 209 | 868 | 1,031 |  |  | 25 | 201 | 290
Brewer | 1,177 | 611 | 203 |  |  | 153 | 82 | 35
Fall Cr. Conf. | 374 | 326 | 258 |  |  | 86 | 37 | 52
Compared to 2013, in 2014:
1% reduction in wetted area
30% increase in water volume
  Thalweg
Still high sediment, compared to 2012
Notes: ADD RANGE

## Slide 30: Area and vol. greater at one location
 | Area (m2) |  |  | Volume (m3) | 
Location | 2012 | 2013 |  | 2012 | 2013
Baumann Slough | 2,960 | 390 |  | 1,472 | 124
Simpson Slough | 63 | 151 |  | 4 | 13
Brewer Slough | 484 | 67 |  | 169 | 11
Fall Cr. Conf. Slough | 1,093 | 963 |  | 135 | 248
Combined:
66% reduction in wetted area
78% reduction in water volume
Sedimentation
Scour
Increase in wetted area and volume
Scour mid-site greater than sedimentation volume near mouth

## Slide 31
Baumann slough 7/19/2012: 152 cfs

## Slide 32
Baumann slough 4/2/2013: 68 cfs

## Slide 33
Baumann slough 4/2/2013: 68 cfs

## Slide 34: Fish results
Year | Oregon chub | Redside shiner | Speckled dace | Sculpin Spp. | Northern pikeminnow | Largescale sucker | Sand roller | Rainbow trout | Brown bullhead | Bluegill | Total
2012 | 7 | 47 | 554 | 35 | 6 | 4 | 4 | 1 | 6 | 1 | 665
2013 | 2 | 7 | 57 | 22 | 2 | 22 | 1 | 15 | 3 | 11 | 142
2014 | 137 | 210 | 125 | 37 | 28 | 21 | 0 | 0 | 0 | 3 | 561
10 species encountered; Oregon chub observed at each location
2013: nearly 80% reduction from 2012 abundance
2014: rebound?
Nonnative species present, but in low abundance

## Slide 35: Conclusions
Concerns:
  Sedimentation has severely reduced the off-channel habitat downstream of Fall Creek Reservoir
  Current managed maximum flows may not have energy required to move fine sediment from floodplain sites.

## Slide 36: Conclusions
Recommendations:
  Seek alternate management
    Completing the drawdown during low flow periods
    Draw down the reservoir, but not to run of the river
  Okay for Fall Creek, would significantly impact habitats in other subbasins

## Slide 37: Future studies
Continue to monitor changes in bathymetry at Fall Creek locations
  Determine long term effect on fish assemblage
  Determine best flow regime for managing this system

## Slide 38: Questions?