## Slide 1
AN EVALUATION OF FISH BEHAVIOR AT THE PORTABLE FLOATING FISH COLLECTOR AT COUGAR RESERVOIR USING ACOUSTIC CAMERAS, 2014
For
Army Corps of Engineers
Willamette Fisheries Science Review
February 11, 2015
Portland, Oregon
Western Fisheries Research Center
Columbia River Research Laboratory
Cook, Washington, USA
Noah Adams, Collin Smith, and Gabriel Hansen
Entrance to PFFC
Trash Boom
U.S. Department of the Interior U.S. Geological Survey

## Slide 2
Goals for 2014
  Use acoustic cameras to quantify fish behavior upstream and inside the PFFC.
    Fry
    Parr
    Smolts
  Estimate number of fish entering and exiting the PFFC and identify areas of rejection.
  Examine predator activity near the PFFC.
30 - 60 mm
60 - 90 mm
90 - 250 mm
> 300 mm
Targets

## Slide 3
Methods
- Equipment
- Data
- Processing
- Tracking
- Analysis
Outline
Results
- Abundance
- Density
- Movements

## Slide 4
Equipment
DIDSON
  1.8 MHz
  14° x 29°
  ~10 m range
  Fish >40 mm
ARIS
  3.0 MHz
  14° x 30°
  ~5 m range
  Fish >30 mm

## Slide 5
Camera Deployment
DIDSON
ARIS
    30 May to 3 December
    Collected 7,500 hours of video.
    ~30 terabytes of data
Scale
3 m

## Slide 6
Data Processing and Analysis
* Target size
* Target density
* Direction
* Speed
* etc….
EchoView software used for semi – automated data processing and tracking.
Video → Digital target → Track
Echogram
Data processing and quantitative analysis methods were developed during 2013.
- More data can be processed
- Processing yields quantitative target information
- Data processing is constant

## Slide 7: Results (for today’s presentation)
- ARIS
    50% of 110 days spread across the season
    (two 15 min. blocks randomly selected for each hour)
- DIDSON
100% of 110 days spread across the season
- Combined
~ 9,500 fish tracks
~ 300,000 individual track data points

## Slide 8: Abundance at PFFC 2014 vs. WTC tower 2013
(DIDSON only)
348
29
72
12
30 - 250 mm
> 300 mm

## Slide 9: Abundance at PFFC by Fish Size
(DIDSON + ARIS)

## Slide 10: Abundance at PFFC by Hour of Day
(DIDSON only)
Fry
Parr
Smolts

## Slide 11
Abundance Inside PFFC
PFFC TRAP CATCH
N = 320
53%
24%
27%
35%
Fish size 30-250 mm

## Slide 12
Abundance Inside PFFC
PFFC TRAP CATCH
N = 320
53%
24%
27%
35%
Fish size 30-250 mm

## Slide 13
Low treatment (~50cfs)
High treatment (~100 cfs)
Fish size 30-250 mm
Aris - 805
Aris - 980
Didson – 2,020
Didson – 3,583
Proportional Density Upstream of PFFC

## Slide 14
Direction of Movement at PFFC
Low
High
* Watson’s Two-Sample Test for Common Distributions
n = 3,532
n = 2,000
p > 0.10
n = 941
n = 758
p > 0.10
Fish size 30-250 mm

## Slide 15
Low treatment - Fish size 30-250 mm
ARIS
Velocity (ft/s)
Direction of Movement Inside PFFC
186
189
237
204
N
Distance from camera (m)
5.0
6.5
3.5
5.75
4.25
36%

## Slide 16
High treatment - Fish size 30-250 mm
ARIS
Velocity (ft/s)
Direction of Movement Inside PFFC
320
124
235
118
N
Distance from camera (m)
5.0
6.5
3.5
5.75
4.25
40%

## Slide 17
Summary
  Median daily observations were much less upstream of PFFC compared to upstream of WTC tower.
    PFFC needs to be moved closer to the tower?
  Predators appear to play a role in deterring juvenile fish from entering the PFFC.
    Consider minimizing predator habitat…. log boom?
  Entrance conditions cause fish to avoid going in the PFFC and the vast majority that did go in turned around and left.
  Modifications to achieve design flows upstream and inside the PFFC should increase capture efficiency.
  Multiple evaluation tools provided valuable information to inform changes that could improve PFFC performance.

## Slide 18
QUESTIONS ?
Acknowledgements
    USGS
    John Beeman, Hal Hansel, Amy Hansen, Scott Evans, Philip Haner, Tyson Hatton, Eric Kofoot, Kyle Martens, Jamie Sprando, Matt Sholtis, Collin Smith, Nick Swyers, Craig Haskell, Glen Holmberg, Russell Perry,
    John Plumb
USACE
David Griffith, Wes Hively, Andrew Janos, Todd Pierce, Mary Karen Scullion