## Slide 1: Evaluation of the Cougar Dam PFFC using acoustic telemetry
John Beeman, Hal Hansel, Amy Hansen, Gabriel Hansen, Scott Evans, Philip Haner, Tyson Hatton, Eric Kofoot, Kyle Martens, Jamie Sprando, Matt Sholtis, Collin Smith, Nick Swyers, Noah Adams
USGS, Western Fisheries Research Center
Columbia River Research Laboratory
Cook, WA 98605
U.S. Department of the Interior U.S. Geological Survey
Willamette Review, February 11, 2015

## Slide 2: Outline
Study fish, monitoring methods
Numbers collected by PFFC, etc.
3 reasons it did not work better
Summary

## Slide 3: Fish and Tags
12 mm PIT tags
  495 on June 4
  1,010 on October 22
  Antennas in PFFC and downstream
Acoustic (0.43 g) + PIT tags
  434 from April 9 – May 21
    (incl. 4 wild)
    144 d tag life (90%)
  4 hydrophones at forebay log boom, 26 in cul-de-sac, others in tower and downstream
Overall catch of medium-size fish (surrogates)
  Spring 65–93 mm FL µ=76.7
  Fall 71–180 mm FL µ=154.5
  Where, What, When, Why
  104–180 mm, µ= 163.6
  Mostly surrogates
What
Why
All fish released near the head of the reservoir

## Slide 4: Operating Conditions
Before (5/16 – 5/27)
Low (~50 cfs) or High (~100 cfs) inflow
  Randomized block schedule, 5/27-10/28
    7-d treatments, 14-d blocks
2.7 m
~ 3 m
PIT antenna
18 m

## Slide 5: Metrics (by the numbers)
Travel Percentages
  % released reaching forebay log boom
  % @ BRZ reaching cul-de-sac
    % of those w/ position estimates
  % cul-de-sac within 10 m & 1 m of PFFC entrance
Total number captured in PFFC
Capture Efficiency (JSATS+PIT only)
  A: PFFC / (PFFC + WTC) ; WTC / (PFFC + WTC)
  B: PFFC / # in cul-de-sac; WTC/# in cul-de-sac

## Slide 6: Where Fish Were: Utilization Distributions
N = 129
Kranstauber et al. 2012. A dynamic Brownian bridge movement
model to estimate utilization distributions for heterogeneous
animal movement. Journal of Animal Ecology 81:738-746.
Low inflow, daytime, 0-3 m depth
Date range May 18 – October 28, 2014
N ≥ 9 obs, gap ≤ 0.5 hour = 1 trip
Dynamic Brownian Bridge Mov. Model
Probability of being in a 5 x 5 m cell
Average within fish, then among fish
Positions to probabilities
UTM Easting(m)
UTM Northing(m)
UTM Easting(m)
Low inflow, daytime, 0-3 m depth
N = 129

## Slide 7: What: Many Fish Within 10 m, Few Nearer
Category | N | Percent
Released | 434 | --
Detected at Log Boom (in total) | 399 | 91.9
Det. @ Log Boom during PFFC ops | 223 | --
Detected in Cul-de-sac | 214 | 96.0
Positioned in Cul-de-sac | 213 | 99.5
Within 10 m of PFFC (@ 0-3 m deep) | 144 | 67.6
Within 10 m of PFFC (@ 0-6 m deep) | 183 | 85.9
Within 1 m of PFFC (@ 0-3 m deep) | 0 | 0
Within 1 m of PFFC (@ 0-6 m deep) | 11 | 5.2
Total
During PFFC
ops (> 5/27)

## Slide 8: What: Few Tagged Fish Collected by PFFC
Category | JSATS + PIT | PIT Only
N Detected in PFFC | 2 | 2
N Captured in PFFC | 1 | 2
N Passing Tower (total) | 42 | na
N Passing Tower (PFFC ops) | 13 | na
Collection Efficiencies |  | 
 | Result | Definition
Collection Efficiency (A) | 7.1% (92.9% at tower) | PFFC/(PFFC+Tower)
Collection Efficiency (B) | 0.5% (6% at tower) | PFFC/# in cul-de-sac
*
* = 3 unique fish
Estimated PIT detection probability ~ 95%

## Slide 9: Why #1a: The PFFC OPS Started Late
PFFC OPS BEGAN

## Slide 10: Why #1b: Fish Deeper in Summer
0-3 m = 55%
3-6 m = 16%
0-3 m = 35%
3-6 m = 24%
0-3 m = 16%
3-6 m = 20%
0-3 m = 11%
3-6 m = 13%
0-3 m = 28%
3-6 m = 15%
0-3 m = 25%
3-6 m = 15%
Depths of acoustic-tagged fish in the cul-de-sac

## Slide 11: Why #2a: Poor PFFC Location
Utilization Distribution
0–3 m depth
Low, High,
Day, Night
were similar
Average of Before,
Low, High ops.

## Slide 12: Why #2a: Poor PFFC Location
Utilization Distribution
3–6 m depth
Low, High,
Day, Night
were similar
Average of Before,
Low, High ops.

## Slide 13: Why #2a: Poor PFFC Location
Utilization Distribution
0–6 m depth
Low, High,
Day, Night
were similar
Average of Before,
Low, High ops.

## Slide 14: Why #2b: Few Fish near Entrance
High Inflow
Day
High Inflow
Night
Low Inflow
Day
Low Inflow
Night
Utilization Distributions of fish within a 20 m radius of the PFFC entrance

## Slide 15: Why #3: Those Nearby Not Attracted
High Inflow, Day
Axes = distance (m) from center of PFFC entrance
Depth <= 3 m
Depth > 3 m
Large circle = start of fish track
Fish within a 20-m radius of PFFC entrance with ≥ 2 positions within a 10 m radius

## Slide 16: Why #3: Those Nearby Not Attracted
High Inflow, Night

## Slide 17: Why #3: Those Nearby Not Attracted
Low Inflow, Day

## Slide 18: Why #3: Those Nearby Not Attracted
Low Inflow, Night

## Slide 19: Why #3: Those Nearby Not Attracted
Low Inflow, Day
10 m radius
0 – 3m depth
5m
4m
Rose plots indicating headings of fish at 0-3 m depth within a 10 m radius of PFFC entrance

## Slide 20: Summary (1 of 2)
Few fish collected by PFFC
Evidence from tagged fish supports “WHY?” =
  Late start
    Fish depths unfavorable in summer
  Poor location relative to fish locations
    Few fish near entrance
  Fish nearby not attracted
    Few closer than 10 m
    Those nearby traveling across rather than towards

## Slide 21: Summary (2 of 2)
Corroborating evidence:
  Unfavorable inflow velocities (previous presentation)
  Rejection within PFFC (next presentation)
Recommendations following modifications
  Position based on existing fish and hydraulic data
  Continue multi-method evaluation
Uncertainties
  Effects of PFFC outflow on fish behavior

## Slide 22: Acknowledgements
USACE:
    David Griffith, Wes Hively, Andrew Janos, Todd Pierce, Mary Karen Scullion
Wild Fish Surrogate Program
    Eric Billman, Rob Chitwood, Karen Cogliati, Carl Schreck
Staff at Leaburg Hatchery
    Seth Morgan, Erik Withalm
Eugene Water and Electric Board
USGS staff
    Craig Haskell, Glen Holmberg, Russell Perry