## Slide 1: Evaluation of Habitat and Flow Relationships for Spring Chinook Salmon Spawning and Incubation in the Middle Fork Willamette and McKenzie Rivers, Oregon
Troy Brandt and Pete Gruendike
River Design Group, Inc.
Corvallis, Oregon
Jarvis Caldwell
HDR Engineering, Inc.
Sacramento, California
CONTRACT NO. W9127N-12-D-0006-03

## Slide 2: Outline
Project need
Transect selection and data collection
SEFA – System for Environmental Flow Analysis
Analysis and preliminary results

## Slide 3: Project Need
2008 BiOp included a reasonable and prudent alternative to further investigate how flow volumes relate to fish habitat for the target ESA-listed species (natural origin spring Chinook and winter steelhead) by life stages.
Project Goal - Determine how UWR spring Chinook salmon spawning/incubation habitat is influenced by changes in flow in the MF Willamette River, McKenzie River, and SF McKenzie River

## Slide 4: Reach Overview - Geography

## Slide 5: Reach Overview - Flows
Willamette BiOp flow targets for September-October spawning period
Actual flows during post-BiOp (2009-2012)

## Slide 6: Project Workflow
Data Collection
Data Processing
Velocity Calibration
Hydraulic Calibration
Habitat Modeling
Transect Selection
Agency
Collaboration
June and
September 2014
Excel, QA/QC
ODFW Review
Results
HSC - Santiam
AWS – By Reach,
By Transect
Reporting
March 31, 2015

## Slide 7: Study Design
3 reaches
10 XS/reach focused on known spawning areas
Transects primarily located in mainstem riffles and side channel habitats
Measured stage and discharge at 3 flows
Measured channel XS, velocity, bed material, and cover

## Slide 8: Study Design – MF Willamette Sections

## Slide 9: Reach Overview – Habitat Conditions
MF Willamette River
Mainstem
Side Channel

## Slide 10: Study Design – McKenzie Sections

## Slide 11: Reach Overview – Habitat Conditions
McKenzie River
Mainstem
Side Channel

## Slide 12: Study Design – SF McKenzie Sections

## Slide 13: Reach Overview – Habitat Conditions
SF McKenzie River
Mainstem
Side Channel

## Slide 14: Project Workflow
Data Collection
Data Processing
Velocity Calibration
Hydraulic Calibration
Habitat Modeling
Transect Selection
Agency
Collaboration
June and
September 2014
Excel, QA/QC
ODFW Review
Results
HSC - Santiam
AWS – By Reach,
By Transect
Reporting
March 31, 2015

## Slide 15: SEFA
System for Environmental Flow Analysis (SEFA)
Instream Flow Incremental Methodology software
2014 - Repackaged PHABSIM/RHABSIM
Also Includes Water Temp, DO, Riparian, Sediment
http://sefa.co.nz/
Notes: System for Environmental Flow Analysis

## Slide 16: Hydraulic Calibration
First step in the modeling process is the hydraulic calibration.
Develop stage-discharge relationship for each transect using measured stage and discharge at the low, mid, and high flow
To reduce mean error between measured and modeled discharges, we made small adjustments to observed stage

## Slide 17: Velocity Calibration
Second step in the modeling process is the velocity calibration
Velocity measured at one flow (mid) per transect
Compare pattern of measured velocities vs. modeled velocities
Correct anomalous velocities with roughness adjustment
We made minimal adjustments

## Slide 18: Model Calibration Results
Predicted discharge vs. Measured discharge
Goal = Mean Error <5%
Fewer calibration adjustments are better
Notes: Mean error in Q relates the difference between measured and predicted discharge when using Hydraulic roughness relationship. Utilizes Manning’s roughness equation and channel shape ( hydraulic radius ) to determine discharge. Validated by stage / discharge rating curve.

## Slide 19: Habitat Suitability Curves
Chinook Spawning – Santiam, 2013
LOW
HIGH
SILT
BOULDER
Notes: Index refers to substrate- classified by dominant and subdominant particle size along with percentage of dominant. Starting at 30 is small gravel, 80 is boulder. Smaller or larger is unsuitable.

## Slide 20: Habitat Modeling - AWS
Combine hydraulic model and habitat suitability criteria to determine Area Weighted Suitability (AWS) by transect
Red – 0.0 Poor Spawning Habitat
Yellow – 0.5 Moderate Spawning Habitat
Blue – 1.0 Optimal Spawning Habitat
Notes: Equal weighting for transects because all assumed to be known spawning habitat. Can weight different transects heavier or lighter if wanted

## Slide 21: Habitat Modeling - AWS
AWS normalized to 1,000 linear feet of stream
Habitat comparison units – square ft/1,000 ft
Equal Transect Weighting – 10 transects at 10%
  Can vary transect contributions – mainstem vs. side channel, habitat units % of total reach
Assess individual and combined sections

## Slide 22: Preliminary Results - AWS
MF Willamette River – Individual Transect Results

## Slide 23: Preliminary Results - AWS
MF Willamette River – Combined Transect Results
Notes: 1800-3000

## Slide 24: Preliminary Results - AWS
SF McKenzie River - Individual Transect Results

## Slide 25: Preliminary Results - AWS
SF McKenzie River - Combined Transect Results
Notes: 350-650

## Slide 26: Preliminary Results - AWS
McKenzie River – Individual Transect Results

## Slide 27: Preliminary Results - AWS
McKenzie River – Categorized Transect Results
Mainstem
Side Channel
Notes: 1500-2200

## Slide 28: Preliminary Results - AWS
McKenzie River – Combined Transect Results
Notes: 1500-2200

## Slide 29: Preliminary Results
Study Reach | BiOp Flow Range (cfs) | (Preliminary) Optimal Flow Range (cfs) | (Preliminary) Optimal Target Flow (cfs)
MF Willamette River | 1,200 – 3,500 | 1,800 – 3,000 | 2,400
McKenzie River | Coincident with SF McKenzie | 1,500 – 2,200 | 1,800
SF McKenzie River | 300 - 580 | 350 - 650 | 519

## Slide 30: Summary
Preliminary optimal flows overlap with BiOp flows
Currently preparing analysis and tech team review
Report due March 2015

## Slide 31: Acknowledgements
USACE
  Dave Leonhardt
  Tim Kuhn
  Mary Karen Scullion
  Greg Taylor
ODFW
  Tim Hardin
  Paul Olmstead
  Cameron Sharpe
  Mike Hogansen
OWRD
  Rachel LovellFord
NOAA-Fisheries
  Rich Domingue